## Slide 1
Evaluation Methods for Climate-SMART Sanitation
Assessment Methods
UPM Umwelt-Projekt-Management GmbH
June 2025

## Slide 2
Agenda
How to assess the Climate-SMART sanitation component?
How to apply the Climate-SMART Sanitation approach on technology
1
2
3
How to apply the Climate-SMART Sanitation approach on system
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment

## Slide 3
1.
HOW TO ASSESS CLIMATE-SMART SANITATION COMPONENTS

## Slide 4
Climate-SMART Sanitation is:
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
4

## Slide 5
Safe
ACCESS TO SANITATION
“JMP SANITATION LADDER”
SHIT FLOW DIAGRAM (SFD)
RISK FOR GROUND WATER POLLUTION
MECHANICAL EMPTYING, PPE, SOPs, VACCINES
OUTPUTS (EFFLUENT, SLUDGE, BY-PRODUCTS) MEET NATIONAL / WHO STANDARDS
BUILDING CODE
COMPLETE TREATMENT, PPE, SOPs, VACCINES
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
5

## Slide 6
Mitigative
IPCC (OR OTHER METHODS IF REQUIRED GOLD STANDARD, …)
ENERGY PERFORMANCE AND CARBON EMISSIONS AND MONITORING TOOL
IPCC (OR OTHER METHODS IF REQUIRED GOLD STANDARD, …)
IPCC (OR OTHER METHODS IF REQUIRED GOLD STANDARD, …)
IPCC (OR OTHER METHODS IF REQUIRED GOLD STANDARD, …)
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
6

## Slide 7
Adaptative & resilient
UTS CLIMATE-FIRST
UNICEF‑GWP RISK ASSESSMENT
UTS CLIMATE-FIRST
UTS CLIMATE-FIRST
UTS CLIMATE-FIRST
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
7

## Slide 8
Transformative
PERCEPTION & ACCEPTANCE STUDY
MARKET DRIVEN APPROACH FOR SELECTION OF FECAL SLUDGE TREATMENT PRODUCT
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
8

## Slide 9
2.
HOW TO APPLY THE CLIMATE-SMART SANITATION APPROACH ON TECHNOLOGY

## Slide 10
Safe
ACCESS TO SANITATION
“JMP SANITATION LADDER”
SHIT FLOW DIAGRAM (SFD)
RISK FOR GROUND WATER POLLUTION
MECHANICAL EMPTYING, PPE, SOPs, VACCINES
OUTPUTS (EFFLUENT, SLUDGE, BY-PRODUCTS,) MEET NATIONAL / WHO STANDARTS
BUILDING CODE
COMPLETE TREATMENT, PPE, SOPs, VACCINES
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
10

## Slide 11
Safe
ACCESS TO SANITATION
“JMP SANITATION LADDER”
RISK FOR GROUND WATER POLLUTION
MECHANICAL EMPTYING, PPE, SOPs, VACCINES
OUTPUTS (EFFLUENT, SLUDGE, BY-PRODUCTS,) MEET NATIONAL / WHO STANDARTS
BUILDING CODE
COMPLETE TREATMENT, PPE, SOPs, VACCINES
SERVICE LEVEL | DEFINITION | SDG | TARGET
SEFELY MANAGED | Use of improved facilities, not shared with other households, with excreta safely disposed of in situ or treated offsite. | 6.2.1a | By 2030, all people should have access to safely managed sanitation services.
BASIC | Use of improved facilities that are not shared with other households | 1.4.1 | By 2030, ensure that all men and women, particularly the poor and the vulnerable, have equal rights to economic resources, as well as access to basic services, …
LIMITED | Use of improved facilities shared between two or more households |  | 
UNIPROVED | Use of pit latrines without a slab/platform, hanging latrines, or bucket latrines |  | 
OPEN DEFICATION | Disposal of human feces in open spaces (fields, forests, water bodies, etc.) or with solid waste |  | End open defecation
Groundwater
pollution
risk
estimation
tool
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
11

## Slide 12
Safe
ACCESS TO SANITATION
“JMP SANITATION LADDER”
RISK FOR GROUND WATER POLLUTION
MECHANICAL EMPTYING, PPE, SOPs, VACCINES
OUTPUTS (EFFLUENT, SLUDGE, BY-PRODUCTS,) MEET NATIONAL / WHO STANDARTS
BUILDING CODE
COMPLETE TREATMENT, PPE, SOPs, VACCINES
VACCINES:
tetanus,
polio,
typhoid fever,
hepatitis A and B
Also, regular health checks &
Treatment (i.e., deworming)
PPE
MECHANICAL
EMPTYING
PPE
Example Occupational Health & Safety Manual
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
12

## Slide 13
Safe
ACCESS TO SANITATION
“JMP SANITATION LADDER”
RISK FOR GROUND WATER POLLUTION
MECHANICAL EMPTYING, PPE, SOPs, VACCINES
OUTPUTS (EFFLUENT, SLUDGE, BY-PRODUCTS) MEET NATIONAL / WHO STANDARDS
BUILDING CODE
COMPLETE TREATMENT, PPE, SOPs, VACCINES
VACCINES:
tetanus,
polio,
typhoid fever,
hepatitis A and B
Also, regular health checks &
Treatment (i.e., deworming)
PARAMETER | WHO GUIDELINE VALUE FOR IRRIGATION
Helminth eggs | ≤ 1 egg/L
Fecal coliforms | ≤1,000 per 100 mL
PPE
Example
Safety
Manual
FSTP
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
13

## Slide 14
Mitigative
IPCC (OR OTHER METHODS IF REQUIRED GOLD STANDARD, …)
ENERGY PERFORMANCE AND CARBON EMISSIONS AND MONITORING TOOL
IPCC (OR OTHER METHODS IF REQUIRED GOLD STANDARD, …)
IPCC (OR OTHER METHODS IF REQUIRED GOLD STANDARD, …)
IPCC (OR OTHER METHODS IF REQUIRED GOLD STANDARD, …)
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
14

## Slide 15
Mitigative
Community Baseline (1,000 people)
70% unlined pit latrines (no flush)
30% open defecation
Emissions: 24,520 kg CO₂ eq/year or 24.5 kg /person)
Scenario 1: Unmitigated Improvement
100% septic tanks + low-flush toilets, with safe effluent infiltration
Emissions: 137,751 kg CO₂ eq/year or 138 kg /person) 6 x Increase!
Scenario 2: Mitigated Composting Toilets
100% composting toilets (well-managed).
Emissions: 597 kg CO₂ eq/year or 0.6 kg/person
230 times lower than unmitigated!
How to estimate the GHG emissions will be explained and practiced during the exercise after the break.
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
15

## Slide 16
Adaptative & Resilient
UTS CLIMATE-FIRST
UNICEF‑GWP RISK ASSESSMENT
UTS CLIMATE-FIRST
UTS CLIMATE-FIRST
UTS CLIMATE-FIRST
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
16

## Slide 17
Adaptative & Resilient
UTS CLIMATE-FIRST
For planning adaptation measures and designing resilient sanitation technologies UTS ClimateFIRST Framework consisting of 5 steps.
STEP 1: SCOPING THE ASSESSMENT
IN Scope: Pit-lining, slab, super-structure, vent pipe
OUT of Scope: Off-site sludge treatment
STEP 3 RATE IMPACTS OF HAZARDS ON SYSTEM COMPONENTS
HAZARDS | RATING | RATIONALE
Flooding | H | Floodwater can enter via superstructure, filling pit; buoyant force may crack lining.
Short dry spells | L | No functional impact.
Extreme heat | L | Minor odor increase; structure unaffected.
Strong wind | M | Lightweight roofs/doors susceptible.
Color key: H = high-impact, M = moderate, L = low
STEP 2 IDENTIFICATION OF HAZARDOUS EVENTS & TRENDS (HETS)
Flooding: riverbank overtopping & flash floods (≤ 1 m depth)
Short dry spells (≈ 1 week): intermittent low inflow & drying
Extreme heat & high THI: >35 °C, THI > 30
Strong gust winds: embedded convective storm bursts
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
17

## Slide 18
Adaptative & resilient
UTS CLIMATE-FIRST
STEP 4: – ADAPTATION MEASURES
AVOID: Elevate slab 0.5 m; seal drop‑hole with flip‑cap.
WITHSTAND: Reinforced outer supports to prevent pit wall collapse from water pressure in the ground. Anchor the roof panels
FLEXIBILITY / FAST RECOVERY: Detachable prefab superstructure for quick swap after storm damage.
CONTAIN: Gasketed pit cap for emergency closure before flood onset.
LIMITING THE CONSEQUENCES OF COMPLETE FAILURE: Add a small, sealed overflow chamber adjacent to the main pit that captures excess sludge during flooding or overfilling, reducing spill risk.
FAST RECOVERY: Utilize modular superstructure panels that can be easily replaced if damaged and install a visible fill-level indicator for quick detection of overflow risk.
PROVIDING BENEFITS BEYOND RESILIENCE: Integrate a hand‑washing tap on the same plinth and use the greywater for irrigation, add a rainwater collection system.
Note: Step 5 of ClimateFIRST (“Judging Overall Resilience”) uses auto-generated scoring from the tool and is not shown here. A download link is available in the resource section.
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
18

## Slide 19
Transformative
PERCEPTION & ACCEPTANCE STUDY
MARKET DRIVEN APPROACH FOR SELECTION OF FECAL SLUDGE TREATMENT PRODUCT
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
19

## Slide 20
Transformative
PERCEPTION & ACCEPTANCE STUDY
Challenging the mindset by embracing circular economy principles—viewing waste as a resource to be recovered, reused, and reintegrated into productive systems.
However, transformation is not solely about resource recovery. A paradigm shift also occurs when a community transitions from no or limited sanitation access to basic and improved services.
 | % WILLING TO USE | KEY CONCERN | WHAT WOULD CHANGE YOUR MIND ? | %
Biogas | 80% | Cookstove to expensive | Free Cookstove | 45 %
PERCEPTION
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
20

## Slide 21
3.
HOW TO APPLY THE CLIMATE-SMART SANITATION APPROACH ON SYSTEM

## Slide 22
Steps to design Climate-SMART Sanitation system
ACCESS TO SANITATION
SHIT FLOW DIAGRAMM (SFD)
SMART BASELINE
ASSESSMENT
ECAM
UNICEF‑GWP RISK ASSESSMENT
MARKET DRIVEN APPROACH
PERCEPTION & ACCEPTANCE
TECHNICAL SOLUTION SCREENING
MCDA
UTS CLIMATE-FIRST
SMART BASELINE IMPROVEMENT VERIFICATION
ACCESS TO SANITATION
SHIT FLOW DIAGRAMM (SFD)
ECAM
UNICEF‑GWP RISK ASSESSMENT
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
22

## Slide 23
Safe
ACCESS TO SANITATION
“JMP SANITATION LADDER”
SHIT FLOW DIAGRAM (SFD)
RISK FOR GROUND WATER POLLUTION
MECHANICAL EMPTYING, PPE, SOPs, VACCINES
OUTPUTS (EFFLUENT, SLUDGE, BY-PRODUCTS,) MEET NATIONAL / WHO STANDARDS
BUILDING CODE
COMPLETE TREATMENT, PPE, SOPs, VACCINES
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
23

## Slide 24
SHIT FLOW DIAGRAM (SFD)
A Shit Flow Diagram (SFD) is a simple, visual tool that shows how human waste flows through a city or community — from where it's generated (toilets), through collection, treatment, and final disposal or reuse. It highlights what proportion of fecal sludge is safely managed versus unsafely managed. SFDs help identify weak points in sanitation systems, support decision-making, and raise awareness among stakeholders about the need for improved sanitation services.
Safe
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
24

## Slide 25
Mitigative
IPCC (OR OTHER METHODS IF REQUIRED GOLD STANDARD, …)
ENERGY PERFORMANCE AND CARBON EMISSIONS AND MONITORING TOOL
IPCC (OR OTHER METHODS IF REQUIRED GOLD STANDARD, …)
IPCC (OR OTHER METHODS IF REQUIRED GOLD STANDARD, …)
IPCC (OR OTHER METHODS IF REQUIRED GOLD STANDARD, …)
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
25

## Slide 26
ECAM
ECAM is an open-source software developed to assess greenhouse gas (GHG) emissions from urban water and sanitation systems. It is aligned with IPCC guidelines, using emission factors and methodologies consistent with global standards. The tool covers the entire sanitation service chain
Mitigative
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
26

## Slide 27
ECAM
It is possible to overlay emissions data onto the SFD, helping visualize both sanitation flows and climate impacts.
SHIT FLOW DIAGRAM (SFD)
Mitigative
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
27

## Slide 28
Adaptative & resilient
UTS CLIMATE-FIRST
UNICEF‑GWP RISK ASSESSMENT
UTS CLIMATE-FIRST
UTS CLIMATE-FIRST
UTS CLIMATE-FIRST
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
28

## Slide 29
UNICEF‑GWP RISK ASSESSMENT
STEP 1: HAZARD IDENTIFICATION
ENVIRONMENTAL (flooding)
BIOLOGICAL/CHEMICAL (groundwater contamination)
HUMAN-INDUCED (poor FSM services)
This Strategic Framework, developed by UNICEF and the Global Water Partnership (GWP), offers a comprehensive approach for integrating climate risks and other stressors (e.g. conflict) into all stages of WASH programming.
STEP 2: EXPOSURE RISK IDENTIFICATION
PHYSICAL (Latrines)
ENVIRONMENTAL (Proximity water source)
SOCIAL (Populations dependent on the system.)
STEP 3: VULNERABILITY ASSESSMENT
PHYSICAL (quality, age infrastructure)
ENVIRONMENTAL (Degradation of water sources, )
SOCIAL (practice, awareness)
FINANCIAL (budget for repairs, insurance)
STEP 4: RISK SCORE CALCULATION
Risk = Hazard × Exposure × Vulnerability
Adaptative & resilient
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
29

## Slide 30
UNICEF‑GWP RISK ASSESSMENT
The risk score can also be combined with the SFD to identify priority interventions.
ECAM
SHIT FLOW DIAGRAMM (SFD)
Adaptative & resilient
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
30

## Slide 31
Transformative
PERCEPTION & ACCEPTANCE STUDY
MARKET DRIVEN APPROACH FOR SELECTION OF FECAL SLUDGE TREATMENT PRODUCT
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
31

## Slide 32
The market-based approach developed by Eawag offers a structured framework for assessing the economic viability and scalability of resource recovery from fecal sludge.
MARKET DRIVEN APPROACH FOR SELECTION OF FECAL SLUDGE TREATMENT PRODUCT
STEP 1: IDENTIFICATION OF RECOVERY PRODUCTS AND SUBSTITUTES
Each product (e.g. solid fuel, liquid fuel, electricity) is compared with a conventional substitute product already established in the market (e.g. charcoal, LPG, grid electricity).
MARKET SIZE ESTIMATION
STEP 2: ESTIMATION OF SUBSTITUTE MARKET SIZE
For each substitute, the annual market volume (in tons, kWh, m³, or units) and the market price are specified. This gives the baseline value of the substitute market.
STEP 3: ADJUSTMENT FOR REALISTIC MARKET CAPTURE
Because reuse products from fecal sludge may differ in quality, availability, or logistics, an adjustment factor is applied (usually <1) in. For biogas the adjustment factor could be purity i.e. 0.7 (because 70% of methane in biogas).
STEP 4 : CALCULATION OF POTENTIAL MARKET SIZE
The adjusted volume is multiplied by the price of the substitute to estimate the realistic market size the reuse product could capture:
Market size = Adjusted volume × Substitute price
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
32

## Slide 33
Technial solution screening
Following the baseline assessment, a comprehensive longlist of potential technical solutions is developed. In this illustrative case, we consider a range of onsite containment options. To systematically evaluate and rank these options, a Multi-Criteria Decision Analysis (MCDA) approach can be applied, using defined scoring criteria and weighted factors, in line with climate SMART approach.
STEP 1: DEFINE SCORING (Example Onsite Containment)
SCORE | SAFE | MITIGATIVE | ADAPTIVE & RESILIENT* | TRANSFORMATIVE
5 | Fully watertight/flood-proof | Net-zero or net-negative GHG | Engineered for extreme events | High-value recovered product or energy
4 | Good containment, minor leak risk | Strong CH₄/N₂O avoidance or capture | Flood-protected components | Valuable soil amendment or fuel
3 | Partial lining | Moderate GHG reduction | Some Flood-protected components | Useful but low-value recovery
2 | No lining | Limited GHG reduction | Minimal adaptation | Little to no recovery
1 | No containment | No benefit or high emissions | Vulnerable | Pure disposal
MCDA
* Note: Adaptive measures can be enhanced over time in alignment with the climateFIRST framework; the current assessment focuses on built-in features.
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
33

## Slide 34
Technial solution screening
Following the baseline assessment, a comprehensive longlist of potential technical solutions is developed. In this illustrative case, we consider a range of onsite containment options. To systematically evaluate and rank these options, a Multi-Criteria Decision Analysis (MCDA) approach can be applied, using defined scoring criteria and weighted factors, in line with climate SMART approach.
STEP 2: SCORE DIFFERENT TECHNOLOGIES
TECHNOLOGY | SAFE | MITIGATIVE | ADAPTIVE & RESILIENT* | TRANSFORMATIVE
Composting Toilet | 5 | 5 | 4 | 4
UDDT | 5 | 5 | 4 | 4
Lined Pour-Flush Pit | 4 | 1 | 2 | 1
Prefab Household Biodigester with Constructed Wetlands | 5 | 5 | 4 | 5
Dry Prefab Pit Latrine | 4 | 2 | 4 | 1
Septic Tank with Constructed Wetlands | 5 | 1 | 4 | 2
MCDA
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
34

## Slide 35
Technial solution screening
Following the baseline assessment, a comprehensive longlist of potential technical solutions is developed. In this illustrative case, we consider a range of onsite containment options. To systematically evaluate and rank these options, a Multi-Criteria Decision Analysis (MCDA) approach can be applied, using defined scoring criteria and weighted factors, in line with climate SMART approach.
STEP 3: WEIGHT THE CRITERIA
CRITERIA | WEIGHT %
Safe | 35
Mitigative | 25
Adaptive / Resilient | 25
Transformative | 15
MCDA
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
35

## Slide 36
Technial solution screening
Following the baseline assessment, a comprehensive longlist of potential technical solutions is developed. In this illustrative case, we consider a range of onsite containment options. To systematically evaluate and rank these options, a Multi-Criteria Decision Analysis (MCDA) approach can be applied, using defined scoring criteria and weighted factors, in line with climate SMART approach.
STEP 3: WEIGHT THE CRITERIA
TECHNOLOGY | SAFE | MITIGATIVE | ADAPTIVE & RESILIENT* | TRANSFORMATIVE | SCORE
Composting Toilet | 1.75 | 1.25 | 1 | 0.6 | 4.6
UDDT | 1.75 | 1.25 | 1 | 0.6 | 4.6
Lined Pour-Flush Pit | 1.4 | 0.25 | 0.5 | 0.15 | 2.3
Prefab Household Biodigester with Constructed Wetlands | 1.75 | 1.25 | 1 | 0.75 | 4.8
Dry Prefab Pit Latrine | 1.4 | 0.5 | 1 | 0.15 | 3.1
Septic Tank with Constructed Wetlands | 1.75 | 0.25 | 1 | 0.3 | 3.3
MCDA
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
36

## Slide 37
Experience sharing
Can you think of any technologies or systems in your country that align with the Climate-SMART Sanitation approach?
Training of Trainers on Climate-Sanitation Nexus – Climate-SMART Sanitation Assessment
37

## Slide 38
Q&A

## Slide 39
19th Floor Jeongdong Bldg. 21-15,
Jeongdong-gil, Jung-gu, Seoul,
Republic of Korea 04518
www.gggi.org
@gggi_hq
@GGGIHQ
@GGGIHQ
@gggi_hq
@GGGIMedia